## Slide 1: Physics 124: Lecture 7
Sensors
(bit incomplete, still)

## Slide 2: Sensing Categories
Voltage
  starting easy: analog in
Distance
  acoustic or light
Speed
  hard; usu. via distance
Acceleration
  accelerometers
Light Level
  phototransistors, photodiodes
Object Passage
  photogate (light source/sense)
Sound Level
  microphone to rectifier?
Temperature
  RTD, thermistor, AD-590
Magnetic Flux
  coil and EMF
Pressure
  pads?
Mass
  spring stretch?
Strain
  strain gauge
http://en.wikipedia.org/wiki/List_of_sensors for overwhelming list

## Slide 3: Voltage
Crudest version is digital: HIGH or LOW: 1-bit resolution
  lots of digital inputs to handle this
  option for internal pull-up resistor to Vcc
Analog in provides 10-bit (0−1023) on Arduino
  considered on crude-to-modest side: 5 mV in 5 V
  high-end is 16-bit (65536 values)
    seldom meaningful to carry more precision than this
  12-bit is also common, and 4× improvement over 10-bit
  8-bit is painful: 0.02 V in 5 V
    but fine for some applications
Voltage is seldom what you fundamentally want to know, but is often the electronic analog of a physical quantity of greater interest
  generally, “converter” can be termed transducer

## Slide 4: Distance
Popular Phys124 metric
  collision avoidance; parallel park; target approach
Acoustic variety
  ultrasound burst and time-of-flight measurement
  Parallax Ping unit is integrated unit, $30
    2 cm to 3 m (dep. on surface type)
  must send 2 ms pulse on SIG pin
  then listen for return pulse
    duration of pulse is round-trip time
  must switch same pin between input/output
  use pulseIn() to measure input duration
Other modules in lab to roll your own acoustic sensor

## Slide 5: Distance via Light?
Not time-of-flight; forget about it! Leave that to pros
Clever sensing of angle between emitter and receiver
Detector is linear array behind lens
  angle maps to position, indicating distance
Smarts on board, so GND, +5 V in; analog voltage out proportional to distance, though not linearly so
Also a proximity version: logic out dep. on “too close”
from http://roborugby.ucd.ie/distsensor.html

## Slide 6: Measure Speed?
Galileo and Einstein would both agree that this is hard to directly sense
Options
  measure distance and rate of change
    noise in distance measurement can make for ratty/spiky velocity
  Doppler?
  measure rotation rate of wheel or axle engaged in motion
    what speedometers do
    can use photogate for once/revolution knowledge

## Slide 7: Acceleration
This is something we can directly sense
Recent rapid advances; driven by MEMs and smartphones
  3-axis accelerometer based on micro-cantilevers capacitively sensed
  bitty MMA7361L unit, $15
    centers output on ½ of 3.3 V
    default roughly ±1.5g, but can config. for ±6g
    zero-g detection and digital flag

## Slide 8: Light Level
Lots of options: phototransistor, photodiode most common
  photons knock electrons loose, which either constitute a base current (phototransistor) or direct into current (photodiode)
Phototransistor (right) effectively has some gain already
  10 kΩ usually about right

## Slide 9: Photodiode Read Out
Many options for photodiode
  reverse bias, developing voltage across resistor
  zero bias, in op-amp feedback mode
Typically < 0.4 A per Watt incident
  stream of photons at 550 nm  0.447 A at 100% Q.E.
  so 1 mm2 detector in full sun (1000 W/m2) is 1 mW
  thus at best 0.5 mA current (puny)
  tend to want pretty large resistor to build up voltage

## Slide 10: Photodiode IV Curve
At zero or reverse bias, current is proportional to incident light power
  note approximate relation: I ≈ 0.4P
  matches quantum expectations

## Slide 11: Object Passage
We often need to know if something is physically present, has passed through, count rotations, etc.
Can have simple scheme of light source and light detector, where the something of interest passes between
  termed a photogate
  interruption of light level pretty unmistakably sensed
  pulse duration, via pulseIn(), may even speak to velocity
Magnetic
  as in bicycle speedometers

## Slide 12: Temperature
Exploit temperature dependence of materials
  RTD: resistive temperature device
    usually laser-etched platinum spiral, often 1000 W + 3.85×(T °C)W
    linear, good absolute calibration
    but a resistor: need to fashion accurate current source and read off voltage (make ohmmeter)
  thermistor: exploits conduction electron density as eT
    nonlinear, due to exponential dependence on T
  AD-590: Analog Devices
    supply 5 V and a route for current (resistor), and output current is proportional to temperature
    measure current as voltage across provided resistor
Caution: resistors often 200 ppm per °C
  for accuracy, may want low “tempco” resistors

## Slide 13: Sound Level
Microphone is transducer for acoustic vibrations into voltage
  usually membrane that vibrates is part of capacitor
  can rectify resulting waveform, low-pass, and measure level

## Slide 14: Magnetic Flux
A loop of wire (or many loops) will develop EMF according to changing magnetic field
  can amplify, rectify, etc.
A Hall sensor can measure DC magnetic field

## Slide 15: Pressure
Pressure pads: 2 conductors separated by carbon film, squeezes out; so more conductivity: bite pads
Capacitive pressure deflects membrane (lab pressure meter)
Party-roller paper tube

## Slide 16: Mass/Weight
“Spring” stretch plus flexometer (strain gauge)

## Slide 17: Strain
Strain gauge can tell you about minute flexing of a structural beam/material

## Slide 18: Other Sensors
Direction
  HM55B Compass Module from Parallax ($30)
Motion
  infrared motion sensor